## Slide 1: Should we rewrite it in a compiled language?
A measured answer · node 24.11 · win32-x64 · dev box, swarm running · taken 2026-07-29

## Slide 2
The instinct is to blame the language
It explains everything, and the fix is heroic.
Notes: Open on the temptation, not the answer. Everyone in the room has felt this.

## Slide 3: So we measured the control plane first
What | Time
pure-JS API route, no I/O | 4-5 ms
API route + one Postgres round-trip | 6-35 ms
dispatch work to a language model | 2,000-120,000 ms
Notes: The controller routes, queues, dispatches and waits. It never calls a model itself.

## Slide 4
A rewrite optimizes the 4 milliseconds
The 30-second wait stays exactly where it is.
Notes: This is the whole argument. Say it once, plainly, and move on.

## Slide 5: Two more reasons it gets worse
The worker CLIs we orchestrate are themselves Node programs — a compiled control plane still ships a JavaScript runtime to run its own workers
The entire browser UI cannot be compiled, because browsers run JavaScript
Scope of the proposal: ~249K lines of TypeScript, 579 end-to-end tests, years of encoded decisions — to chase 4 ms
Notes: Two runtimes instead of one is the detail that usually lands hardest.

## Slide 6: But the same profile found the exception
Chart: 
| superTrendM11 | dmiAdx | adaptiveLaguerre | dmiWave | chandelierBands | movingMedian
But the same profile found the exception | 274 | 180 | 135 | 116 | 116 | 97
Notes: One numeric layer: 1245 ms for 200,000 bars. Fifteen passes over every bar.

## Slide 7: What that costs in practice
10 s
one five-year 1-minute series
1 hour
a 500-combination parameter sweep
900 lines
of pure arithmetic, no I/O
Notes: Real money, and the ideal port target: small, numeric, no I/O.

## Slide 8: Ported to Rust: the numbers
Bars | Before | After | Speedup | Across runs
25,000 | 90 ms | 16 ms | 5.6x | 3.7-7.7x
100,000 | 376 ms | 56 ms | 6.7x | 4.9-9.1x
400,000 | 1474 ms | 250 ms | 5.9x | 4.4-8.5x
Notes: Quote the range, never the peak. One run read 11.1x; repeats put it near 5x.

## Slide 9
Defensible summary: 5 to 7 times
On a 39KB WebAssembly module — with identical results.

## Slide 10: Bit-exact, not close enough
0 ULP
all 40 output series identical
88
tests with the kernel present
6
fallback assertions when absent
Notes: Reachable only because three transcendental constants are computed JS-side and passed in.

## Slide 11: Four decisions that made a second implementation safe
1
Cross the language boundary once per run
never once per calculation
2
Verify bit-exactness
an epsilon hides real divergence
3
Name the reference implementation
when they disagree, the port is wrong
4
Make it optional
nobody else inherits the toolchain
Notes: Boundary-per-bar is the mistake that usually kills this kind of project outright.

## Slide 12: The bug the guard caught on its first run
The kernel relied on "unwritten output slots read zero" — true in the original, which allocated fresh arrays per call
The new loader REUSED its output buffer, for speed
Correct on the first call, wrong on every call after, and no error either way
Only reproducible when a smaller input follows a larger one
Notes: An approximate-tolerance test passes this. That is the argument for exactness.

## Slide 13: Compiled or just better laid out?
What actually won
columnar arrays instead of objects
no per-bar allocation
one reused output buffer
Only then
registers, no boxing, inlining
Notes: The first three are reachable in plain TypeScript. Say so out loud.

## Slide 14: What we are not claiming
Measured on a busy machine — the baseline swung 2.1x between identical runs; no idle-host or Linux number exists yet
One subsystem in isolation, not an end-to-end backtest
Copying results out of the module costs about half the gain
Benchmark input is a seeded random walk — not a market simulation, and no strategy result
Notes: Lead with limits before anyone has to ask. This slide is why the rest is credible.

## Slide 15
The transferable lesson
Profile first. Most systems are waiting, not computing.

## Slide 16: Next steps
Try columnar typed arrays in TypeScript before porting anything else
Measure on an idle host, and on Linux
github.com/emeraldcoastsystemsgroup/oshal